## Welding Safety Test 2014

Directions: Scantrons will be used when taking this test.  Do Not Make Any Marks On This Test Paper.  Students with 5 or less missed on this test will be allowed to weld in the class upon completion of the rewrites.

# Electric Arc Section

- To avoid accidents while working around the welding bench, always keep electrode stubs off the:

  - Table

  - Bench

  - Floor, and in the rod can

  - Equipment

- If the skin is exposed to the electric arc, it will be burned similar to a sunburn.  For this reason you should use:

  - A helmet

  - Gloves

  - Protective clothing

  - All of the above

- If the electrical connections, cable, or electrode holder becomes hot, shut off the welder and:

  - Report this to the instructor immediately

  - Report this to the instructor when convenient

  - Report this to the shop foreman

  - Report the problem to the electrician

- The person responsible for the adjustment of the stick (arc) welding machine is the:

  - Other students

  - The instructor

  - Student in the class, (operator)

  - Electrician

- While performing any welding process, hands should be protected with:

  - Talc powder

  - Another piece of metal

  - A rag

  - Gloves (gauntlet style)

- When chipping slag from the weld you must wear:

  - Shoes

  - Clothes

  - Safety glasses that are ANSI approved

  - Hard hat

- The principle result to exposure (shock) of direct welding current is:

  - Paralyzing the muscular tissues

  - Serious burn

  - Radiation around contact area

  - All of the above

- The greatest potential hazard to all who work with electrical equipment in exposure to:

  - Electric shock

  - Fumes

  - Infrared rays

  - Invisible radiation

- Arc Welding must only be done in booths unless you:

  - Have to do it elsewhere

  - Want to do it elsewhere

  - Obtain the instructor’s approval

  - Obtain the instructor’s approval and use a portable welding screen

- When there is high enough voltage to overcome the resistance and sufficient flow of amperage through a vital path in the body:

  - A serious burn will result

  - Arc welding can still occur

  - Death may result

  - All of the above may occur

- When welding on material which contains zinc, lead, cadmium or fluorine:

  - Have good ventilation

  - Use low hydrogen electrodes

  - Use inert gas rather than stick electrodes

  - Have a fire extinguisher handy

- Welding operators are subjected to eye injuries caused by:

  - Foreign bodies in the eye

  - Welder’s flash burn

  - Radiation and infrared rays

  - All of the above

- Before leaving heated metal unattended, you should use chalk or soapstone to label it with the word “HOT” because:

  - Someone may be burned if he/she touches it

  - Other work may be placed on it

  - You can tell who it belongs to

  - Chalk will help cool it

- As with any electrical device, arc welding and arc welding equipment should not be used in:

  - Darkness

  - A grounded condition

  - A wet area

  - A no load period

- Personal clothing that is acceptable for welding is:

  - Any street clothes

  - Wool or cotton clothing

  - Synthetic clothing

  - Nylon clothing

- When arc welding with stick electrodes in the range of 75 to 100 amps; the shade of lens to be used is a:

  - #3

  - #5

  - #10

  - #14

- When welding and using shielding gases such as argon, helium, carbon dioxide, make sure:

  - You have adequate ventilation

  - You wear gloves

  - Your work is properly lighted

  - You use only tungsten electrodes

- When you are through using the electrode holder (stinger), you should remove the electrode and:

  - Place it on the metal bench

  - Hang the electrode stinger on the hook provided

  - Clamp it on the metal frame

  - Lay it on the floor so students trip over it

- Safety glasses must be worn at all times in class because:

  - Safety glasses are required at all times

  - Eyes are vulnerable to foreign material such as sparks and metal particles

  - Vision impairment is an expensive liability for the welding industry

  - All of the above

- The procedure for placing metal in the bin after welding is:

  - Cool it in the water bin, then place it outside

  - Carry it with tongs, cool it in the water bin, then place it outside

  - Place it outside without tongs

  - Leave it in the booth

Welding Safety Test

Flame Welding Section

- Before using the welding equipment, you must obtain permission from the:

  - Custodian

  - No one

  - The instructor

  - Lab assistant

- The recommended line pressure for acetylene in the RHS Weld Shop is:

  - 5 psi

  - 10 psi

  - 15 psi

  - 25 psi

- Anyone gas welding, brazing or watching the cutting torch flame they must:

  - Squint without welding goggles

  - Wear sunglasses

  - Wear appropriate welding goggles

  - Wear an arc welding helmet with shade lens of 12

- The gas welding or cutting torch should be ignited with a:

  - Match

  - Friction lighter/ striker

  - Pocket lighter

  - Flint

- After you have finished welding, turn off the torch and:

  - Close the valves on the manifold or cylinders

  - Bleed the valves on the torch body

  - Back off the regulator adjusting screws

  - All of the above should be done during the shutdown procedure

- Welding on a tank that has contained flammable liquids is:

  - Easy to do

  - Never done in this shop

  - Done sometimes in this shop

  - Done depending on your skills

- The “working” pressure on the acetylene regulator should never exceed:

  - 5 PSI

  - 10 PSI

  - 15 PSI

  - 24 PSI

- When using an acetylene cylinder, the wrench handle (cylinder valve) must always be kept:

  - In your hand

  - On the cylinder valve at all times

  - Near by

  - In the tool box of the work truck

- You should check connections for leaks on welding equipment with:

  - A match

  - Your ear

  - A spray bottle of soap and water

  - Your hand

- You must report all leaks of cylinders and connections immediately to the:

  - Secretary

  - Lab assistant

  - Instructor

  - Welder nearest you

- Cylinders (Oxygen and Acetylene) are required by law to be:

  - Chained against a wall or solid structure

  - Standing in the vertical position

  - Have the safety caps installed during transportation

  - All of the above

- Due to the heat from the open flame, point the welding torch:

  - Down and away

  - At someone else

  - At the welding hose

  - Up in the air

- When oxy-acetylene welding or cutting, the shade lens to be used is a:

  - #1

  - #5

  - #9

  - #11

- When using high pressure cylinders such as oxygen, the valves should be opened:

  - No more than one turn

  - No more than five turns

  - No more than six turns

  - All the way open

- Oxygen should be used for:

  - Operating pneumatic tools when air is not available

  - Dusting clothing or work

  - Welding or cutting only

  - All of the above at any time

- The maximum amount that acetylene cylinder valves should be opened is:

  - One full turn is recommended

  - Two full turns to restrict flow

  - No more than three turns

  - All the way open

- If an acetylene cylinder develops a leak and it cannot be closed by tightening the cylinder valve:

  - Set the cylinder outside the building away from any possible fire source

  - Notify the instructor

  - Use the welders emergency stop leak

  - Both a and b

- If in doubt about any welding operation and you are not sure of yourself:

  - Stop and don’t do it

  - Research the procedure via text book or reference source

  - Check with the instructor

  - All of the above are recommended

- You should make sure gas welding regulators and equipment are:

  - Lubricated with oil

  - Cleaned with lacquer thinner

  - Kept free of oil and grease

  - Painted

- When a welding torch backfires (pops and blows itself out), you should:

  - Close the oxygen needle valve first

  - Close the acetylene needle valve first

  - Drop the equipment and run for the hills

  - Inspect the equipment and continue

Welding Safety Test

### General Information

- Before starting any welding process in the shop, you should:

  - Rely on the previous class and get right to work

  - Inspect the work area and equipment

  - Comb your hair and look pretty during shop time

  - All of the above

- The GMAW process requires a minimum shade lens of:

  - # 5

  - # 8

  - # 10

  - # 12

- Sharp or crushing points on a piece of equipment are also known as:

  - Pinch points

  - Bullets

  - Instructions

  - Rollers

- A chipping hammer is used to:

  - Prepare edges for welding

  - Remove scale from steel

  - Remove slag

  - Temper beads

- Fire extinguishers for welding areas should be suitable for:

  - Class A fires

  - Class B fires

  - Class C fires

  - All of the above

- It is very important to wear face protection when using a chisel because:

  - A chip of metal may hit you

  - The hammer head is likely to come off

  - Chisels frequently break in half

  - Sight is improved by good face shields

- If a welder is skilled, he/she may repair damaged cylinders in their own shop.

  - True

  - False

- Matches should not be carried in a person’s clothing while welding.

  - True

  - False

- Oxygen will burn violently.

  - True

  - False

- Safety glasses must be Z87 rated to industrial standards to qualify for use in the welding shop.

  - True

  - False